I3201

DISCUSS ITEMS

SSE approach procedures (configuration, airspeeds/power in the descent, and descent rate), SSE circling approach/missed approach, emergency voice reports, in-flight damage/bird strikes, and partial panel/ESIS approach, propeller system/malfunctions.

SSE Approach Procedures (Configuration, Airspeeds/Power in the Descent, and Descent Rate)

Recommend slowing to 120 KIAS at dual engine configuration point for any given approach.

See table for configuration point(s).

Retract the gear/flaps if necessary to maintain profile.

Ensure landing checklist complete prior to 1 mile from threshold or the 90.

110 KIAS minimum until over the threshold. Caution 4 KIAS lost immediately when props are placed full forward.

|  | Precision | Non-Precision | PAR | ASR | LNAV/VNAV, VDA |
| --- | --- | --- | --- | --- | --- |
| NORMAL | 1 ½ dots below GS at GS intercept altitude or 3 NM prior to FAF | 3 NM prior to FAF | Base or Dog-leg to Final | Base or Dog-leg to Final | 1 ½ dots below glidepath at appropriate intercept altitude or 3NM prior to FAF |
| EMERGENCY (SSE) | ½ dot below GS at GS intercept altitude | In safe position to land | 10 Sec gear warning | 10 sec gear warning Safe position to land | ½ dot below GP at appropriate intercept altitude or approaching FAF Safe position to land |

SSE Circling Approach/Missed Approach

Emergency Voice Reports

MAYDAY – Distress. Life-threatening situation. Top priority on all frequencies.
	Derived from French venez m'aider “come help me”

PAN-PAN – Urgency. Not life-threatening system failure, but in need of assistance and priority handling.
	Derived from French panne “breakdown”

AIM 6-3-2

Transmit a distress or urgency message consisting of as many as necessary of the following elements, preferably in the order listed:

(a) If distress, MAYDAY, MAYDAY, MAY− DAY; if urgency, PAN−PAN, PAN−PAN, PAN−PAN.

(b) Name of station addressed.

(c) Aircraft identification and type.

(d) Nature of distress or urgency.

(e) Weather.

(f) Pilots intentions and request.

(g) Present position, and heading; or if lost, last known position, time, and heading since that position.

(h) Altitude or flight level.

(i) Fuel remaining in minutes.

(j) Number of people on board.

(k) Any other useful information.

FTI

The emergency report should include as much of the following information as applicable, time permitting:

i. Declaration of emergency or MAYDAY.

ii. Identification.

iii. Souls on board.

iv. Nature of distress or urgency.

v. Weather.

vi. Intentions.

vii. Present position and heading, or if lost, last known position, time, and heading since that position.

viii. Altitude.

ix. Fuel remaining in hours and minutes for ATC and total quantity for firefighting preparation.

x. Any other useful information.

Do not sacrifice aircraft control to give the emergency report. If time is critical, accomplish the first three items as a minimum.

In-Flight Damage/Bird Strikes

15.23 IN-FLIGHT DAMAGE

If the aircraft should sustain damage because of a midair collision, bird strike, or overstress, the single most important concern is maintaining or regaining aircraft control. Monitor engine and flight instruments for unusual indications.

1. Check controls for freedom and correct response.

2. Prior to landing, a landing configuration check should be conducted above 5,000 feet. The aircraft should be checked for controllability in the landing configuration by slowly decreasing airspeed in 10-knot increments to determine the minimum airspeed at which the aircraft can be safely controlled for landing.

3. Land as soon as possible with minimum control movement.

WARNING

• Careful consideration should be given before making any configuration changes.

• Airframe deformation may significantly increase stall speed.

• Fly approach a minimum of 10 knots above minimum controllable speed to provide a safe margin for landing and possible waveoff.

15.23.1 Spin/Out of Control Flight Recovery

*1. Power Levers — Idle

*2. Rudder — Full deflection in the opposite direction of turn needle

*3. Control Wheel — Rapidly forward

*4. Rudder — Neutralize after rotation stops

*5. Control wheel — Pull out of dive by exerting smooth, steady back pressure.

WARNING

• Abrupt pullout during spin recovery could result in excessive wing loading and a secondary stall or structural damage.

• Do not exceed 3g's during pullout in a clean configuration or 2g's if flaps are fully extended.

15.23.2 Cracked Windshield

1. If it is positively determined that the crack is on the external panel, no immediate action is required.

CAUTION

Windshield wipers may be damaged if used on a cracked outer panel.

Note

• Heating elements may be inoperative in area of crack. Pulling the circuit breaker for the pilot window and selecting BOTH on the WINDSHIELD HEAT SWITCH will allow heating of the copilot window if needed.

• To aid in determining whether the inside or outside pane is cracked, use a pencil. The crack on the inside may be felt. The crack on the outside may be determined by placing the pencil on the crack and looking at the crack from a different angle. If the crack moves, the crack is on the outside (parallax).

2. If the crack is on the inner panel of windshield or cannot be determined, gradually descend and slowly depressurize the aircraft to 2.5 psi or less differential pressure within 10 minutes. Visibility through the windshield may be significantly impaired.

15.23.3 Cracked Cabin Window

If a crack appears in a cabin window, depressurize the aircraft and/or descend to a lower altitude.

Partial Panel/ESIS Approach

FTI APPENDIX B

Dual AHRS Failure (T-44C): In flight, if both AHRS fail.

“I have lost my AHRS. How is yours?”

[IP states his has failed as well]

“Are we able to proceed VMC?”

[IP will respond “yes” or “no.” If “no,” continue.]

“Check the circuit breakers and the reversionary panel.”

[IP will respond with status of both]

“I am on the ESIS, turn off the ‘big five,’ are you familiar with the characteristics of the wet compass?

[IP will respond “yes” or “no.” If ”no,” you must brief the wet compass characteristics.]

“Call out my cardinal headings and update my ESIS heading when I rollout. You have the comms, declare an emergency, and request no-gyro vectors for a PAR/ASR.”

Dual Primary Flight Display Failure (T-44C):

“I have lost my PFD. How is yours?”

[IP states his has failed as well]

“Are we able to proceed VMC?”

[IP will respond “yes” or “no.” If “no,” continue.]

“Check the circuit breakers and the rheostats.”

[IP will respond with status of both]

“I am on the ESIS, you have the comms, declare an emergency, and request no-gyro vectors for a PAR/ASR.”

Propeller System/Malfunctions

Blade Angle Ranges:

Normal 	83* to 15*

Beta 	15* to -5*

Reverse 	-5* to -11*

2.8 PROPELLERS

A three-bladed aluminum propeller is installed on each engine. These propellers are hydraulically controlled, constant-speed, full-feathering, and reversible. Each propeller is controlled by engine oil acting through an engine-driven propeller governor (Figure 2-4). Feathering is accomplished by the feathering springs assisted by centrifugal force applied to the blade shank counterweights. Governor-boosted engine oil pressure moves the propeller blades to the high rpm (low-pitch) hydraulic stop and into reverse pitch. Low pitch propeller position is determined by a mechanically actuated hydraulic stop.

2.8.1 Feathering Provisions

The aircraft is equipped with both manual and automatic propeller feathering. Manual feathering is accomplished by pulling the corresponding propeller lever aft past a friction detent. To unfeather, the propeller lever is pushed forward into the governing range. Feather springs and counterweights will normally feather the propeller anytime there is loss of boosted propeller governor oil pressure, including engine shutdowns on the ground and during any situation in which the propeller is not turning. An automatic feathering system, if armed, will sense loss of torque oil pressure and will feather an unpowered propeller. Automatic feathering can occur only when the propeller AUTOFEATHER switch is in the ARM position, both power levers are at a position that would normally correspond to 90 ±2 percent N1 or greater, and the torque value of one engine drops below 260 ±50 ft/lb. The autofeather system has a cross-interlocking safety feature designed into the control circuit to prevent automatic feathering of both propellers. Before a propeller feathers automatically, the interlock disarms the autofeather circuit of the opposite propeller. After feathering has occurred for one propeller, the opposite propeller can be feathered only by the manual control.

Note

Right propeller may not fully feather with propeller sync on.

2.8.1.1 Propeller Autofeather Switch

Autofeathering is controlled by a propeller AUTOFEATHER switch on the left subpanel. The three-position switch is placarded ARM, OFF, and TEST and is spring loaded from TEST to OFF. The ARM position is used during takeoff, landing, and at the discretion of the Aircraft Commander. If an engine loses power with the system armed and the power levers at or above a position corresponding to 90 ±2 percent N1, two torque-sensing switches 410 ±50 ft/lb and 260 ±50 ft/lb of the affected engine are actuated by loss of torque pressure. Switch actuation applies current through an autofeather relay to a corresponding dump valve, causing the release of oil pressure that holds an established pitch angle on the blades of the affected propeller. Following the release of oil pressure, feathering movement is accomplished by the feathering springs assisted by centrifugal force applied to the blade shank counterweights. The TEST position of the switch enables the pilot to check readiness of the autofeather systems below 90 ±2 percent N1 and is for ground checkout purposes only.

2.8.1.2 Autofeather Lights

Two green lights on the annunciator panel (Figure 12-1), placarded LH or RH AUTOFEATHER ARMED, when illuminated indicate that the autofeather system is armed. Complete arming of the system is accomplished when both power levers are advanced to or above a position corresponding to 90-percent N1 and the autofeather switch is in the ARMED position. Both lights will then illuminate indicating a fully armed system. Both lights will be extinguished if either propeller has been autofeathered or if the system is disarmed by retarding a power lever.

2.8.2 Propeller Synchrophaser

The propeller synchrophaser system is designed for in-flight use only. When in use, the system will automatically “slave” the right propeller rpm to the left “master” propeller. This is accomplished via a magnetic speed pickup mounted in each propeller overspeed governor and magnetic phase pickups mounted on each propeller deice slip ring that transmits electronic pulses to a control unit. The control unit converts any pulse rate differences into correction commands and these correction commands are then transmitted to an actuator motor mounted on the right engine. The actuator motor then “trims” the right propeller governor assembly to exactly match the left propeller rpm while leaving the propeller control lever position constant. If the synchrophaser system is unable to adjust the right propeller to the left, the actuator has reached its travel limit. To recenter the actuator, use the following procedure.

1. PROP SYNC switch — OFF.

2. Synchronize the propellers manually.

3. PROP SYNC switch — ON.

Note

The recentering process will take approximately 6 seconds.

To prevent the right propeller from losing excessive rpm if the left propeller is feathered while the synchrophaser is in use, the system is limited to ±30 rpm from the governor setting. Adjustment of rpm with both propeller levers at the same time will retain the right propeller governor setting within the ±30 rpm range of the left propeller.

2.8.2.1 Propeller Synchronization Switch

One two-position switch located on the control quadrant is placarded PROP SYNC ON — OFF and completes the circuit for propeller synchronization. When the switch is placed in the OFF position, the actuator will automatically run to the center range before stopping. This assures the control will function normally when the ON position is next selected. System operation requires synchronization of the propellers in the normal manner and then selecting ON position of the PROP SYNC switch.

2.8.2.2 PROP SYNC on Light (Annunciator)

The propeller synchronization system is designed for in-flight use only; therefore, if the system is in use and the landing gear is extended (as in an approach for landing), a yellow annunciator light placarded PROP SYNC ON will illuminate.

2.8.3 Propeller Governors

Each propeller system utilizes two governors, one “primary” and one “backup,” to control propeller rpm. Each propeller lever establishes rpm for the respective propeller by altering the setting of a primary governor (Figure 2-4) attached to the propeller gear reduction housing. It is the primary governor that controls rpm through the entire range. Should a primary governor malfunction (exceeding 2,200 rpm by more than 4 percent), an overspeed governor cuts in (2,288 ±40 rpm), dumping oil from the propeller to prevent rpm from exceeding safe limits. If a propeller should stick or move too slowly during a transient condition, the corresponding governor would be unable to prevent an overspeed condition. To provide for this contingency, the pneumatic section of the primary governor acts as a fuel topping governor when the propeller rpm exceeds 2,332 rpm (2,200 rpm + 6 percent). This limits the fuel flow into the engine, thereby reducing the power driving the propeller. During propeller operation in the reverse range, the pneumatic section of the primary governor will be reset to allow a maximum of 2,100 rpm.

2.8.3.1 Propeller Governor Test (PROP GOV TEST) Switch

One two-position switch on the left subpanel (FO-1) is provided for operational test of the propeller systems. The switch is placarded PROP GOV TEST. A solenoid actuated by the PROP GOV TEST switch enables the overspeed governor to be reset for test purposes (1,900 to 2,100 rpm.) The propeller governor test circuit(s) are protected by a circuit breaker placarded PROP GOV located in the ENGINE group on the copilot outboard subpanel.

2.8.3.2 Propeller Levers

Two propeller levers on the control pedestal (Figure 1-4) placarded PROP are used to regulate propeller speeds. Each lever controls a primary governor that acts to regulate propeller speeds within the normal operating range of 1,800 to 2,200 rpm. The full forward position is placarded TAKEOFF, LANDING AND REVERSE, and also HIGH RPM. Full aft position is placarded FEATHER. When a lever is placed at HIGH RPM, the propeller may attain a static rpm of 2,200, depending upon power lever position. With the power levers at idle and the condition levers at low idle, propeller rpm should read between 900 and 1,100 rpm. As a lever is moved aft, passing through the propeller governing range but stopping at the feathering detent, propeller rpm will correspondingly decrease to the lowest limit. Moving a propeller lever aft past the detent into FEATHER will feather the propeller.

Note

If propeller rpm does not read between 900 and 1,100 rpm with the power levers at idle and condition levers at low idle, perform a low pitch torque check (checkflight item 5 in paragraph 10.6) to ensure propeller flight idle stops are correctly adjusted.

2.8.4 Propeller Reversing

CAUTION

• Moving the power levers aft of IDLE without the engine running will result in damage to the reverse linkage mechanism.

• To prevent damage to reversing linkage, propeller levers must be in HIGH RPM position prior to propeller reversing.

The propeller blade angle may be reversed to shorten landing roll. To reverse, propeller levers are positioned at HIGH RPM (full forward) and the power levers are lifted up to pass over the IDLE detent, then pulled aft into REVERSE setting.

2.8.4.1 Propeller Reverse Not-Ready Annunciator Light

One yellow caution light, placarded REV NOT READY, on the annunciator panel alerts the pilot not to reverse the propellers. It illuminates when the landing gear selector handle is down and the propeller levers are not at the HIGH RPM (full forward) position.

15.14 PROP FAILURE

15.14.1 Primary Governor Failure/Malfunction

Normally, the primary governor controls prop speeds within the range of 1,800 to 2,200 rpm. If the prop governor fails, the prop will either feather or overspeed. An uncommanded and uncontrollable prop overspeed greater than 2,200 rpm indicates failure of the primary governor. If the primary governor fails in the overspeed condition, the overspeed governor will maintain a maximum prop speed of 2,288 ±40 rpm, but may not control minimum blade angle. If the governor fails in the feather condition, thrust will be lost, torque will increase, prop rpm will decrease. The increase in torque and decrease in rpm is dependent upon the power setting at the time of failure. With climb power applied when the uncommanded feather occurs, the torque may exceed 2200 ft-lb and the prop may still be turning as high as 1100 rpm until power is reduced. Certain failures of the primary governor will cause the speed control as well as the minimum blade angle control (beta valve) to be inoperative. In this case, aircraft control will be marginal at lower airspeeds and lower engine power settings. Landing with an overspeeding prop is therefore strongly discouraged. However, if forced to land with an overspeeding prop, extra airspeed should be carried on final. This will increase rudder authority while reducing the probability of the prop going into beta in flight. Should the prop blades become jammed during engine power addition, the pneumatic section of the primary governor will act as a fuel topping governor as prop speeds exceed 2,332 rpm. If prop rpm is out of the normal governing range, proceed as follows:

*1. Attempt to adjust prop rpm to normal operating range by manipulating the prop lever. If normal rpm limits

are restored, continue operation. If normal governing range cannot be maintained, as soon as practicable

accomplish the following:

†*2. Power lever — IDLE.

†*3. Prop lever — FEATHER.

WARNING

Prop rpm exceeding 2,420 may result in reduction gearbox failure and/or NP turbine damage.

Note

• The engine with the disabled prop may be operated to provide electrical power.

• The right prop may not fully feather with the prop sync on.

• A fully feathered prop will still be turning at approximately 200 rpm with the engine running.

*4. Alternate Prop Feathering Checklist — As required.

15.14.2 Prop Linkage Failure

If the prop governor control linkage fails, the affected prop will go to 2,200 rpm or maintain the last rpm setting. If a prop linkage failure is suspected, proceed as follows:

1. Manipulate the prop lever to positively determine if the cockpit-prop control is lost.

2. If cockpit prop control is lost and rpm remains within safe limits, match the opposite prop's speed with the

uncontrolled one and land as soon as practicable.

CAUTION

Reversing without the props being in high rpm may damage the reversing linkage.

15.14.3 Alternate Prop Feathering

If the prop linkage or governor fails and when the prop has not feathered by itself or the normal feathering procedures are ineffective, the prop can be feathered utilizing the autofeather system. In this situation, should a need for feathering arise, proceed as follows:

†1. Condition lever (failed prop) — FUEL CUTOFF.

2. Autofeather — ARMED (LS).

3. Power levers — Above 90 percent N1 position (PF).

WARNING

A positive single-engine rate of climb will not be obtained in any configuration with the inoperative engine prop windmilling.

Note

Do not pull the power lever to idle during the autofeathering sequence as the autofeather system would be disarmed while feathering.

4. Emergency Shutdown Checklist — Execute (PF).

***Be prepared to discuss the oil system whenever discussing engine or propeller systems***

2.4 OIL SUPPLY SYSTEM

The engine oil supply (Figure 2-2) is contained in an integral oil tank located between the engine air inlet area and the accessory case. Engine oil cools and lubricates the engine, operates the propeller pitch change mechanism and engine torquemeter system. The system capacity per engine that includes the oil tank, lines, and oil cooler is 14 quarts. The dipstick is attached to the oil filler cap and indicates oil lever in HOT and COLD U.S. quart increments. Recommended oil grade, specifications, capacities, and servicing point are shown in Figure 3-1.

2.4.1 Oil Pressure Pump

Pressure oil is circulated from the integral oil tank through the engine lubrication and propeller system by a self-contained gear-type pressure pump located in the lowest portion of the oil tank. The oil pump consists of two gears and is driven by an accessory gearshaft that also drives the four scavenge pumps. Engine oil pressure is regulated by a pressure relief valve that returns all oil in excess of the regulated pressure to the oil tank.

2.4.1.1 Oil Pressure Transmitter

Main oil pressure is measured from the delivery side of the oil pump and is transmitted to the indicator by the oil pressure transmitter located at the 3-o'clock position on the accessory cowling or engine nacelle.

2.4.2 Engine Oil Cooling

The oil system of each engine is coupled into a heat exchanger unit of fin-and-tube design. These exchanger units are the only airframe-mounted part of the oil systems and are attached to the nacelles below the engine air intake. As oil is returned from the various integral oil pickups, it is returned via the four scavenge pumps to the oil cooler. Air passing through the oil cooler cools the engine oil to the proper temperature range. Normal oil temperature is 10 to 99 °C and is maintained at the proper temperature by a thermal sensor that controls a bypass valve allowing some oil to bypass the oil cooler.

2.4.3 Magnetic Chip Detector

A magnetic chip detector plug is installed in the bottom of the reduction gearbox housing, adjacent to the inlet where oil scavenge from the reduction gearbox commences. The purpose of the chip detector plug is to warn the pilot of ferrous metal in the oil and a possible engine failure. The sensor is an electrically insulated gap immersed in the oil, functioning as a normally open switch. If a large metal chip or a mass of small particles bridge the detector gap, a circuit is completed, sending a signal to illuminate the annunciator panel red light placarded LH or RH CHIP DETECT and the fault WARNING light. The chip detector circuits are protected by the respective circuit breakers placarded CHIP DETECTOR on the right sidewall circuit breaker panel.

15.9 OIL SYSTEM FAILURE

An oil pressure indication below 85 psi is undesirable and should be tolerated only for the completion of the flight. Closely monitor the engine instruments and engine nacelle for secondary indications. Consideration should be given to shutting down the engine and landing as soon as possible; otherwise, reduce power on the engine and land as soon as practicable. Oil pressure below 40 psi and/or temperature that exceeds 99 °C is unsafe and requires that either the engine be shut down or a landing be made as soon as possible using minimum power to sustain flight. In either case, the discrepancy must be noted on the appropriate maintenance form for correction prior to the next flight.

15.9.1 Chip Detector Light Illuminated

Illumination (or flicker) of the CHIPDETECT light indicates that metal particles may be present in the prop reduction gearbox. In the event of a CHIP DETECT light illumination, engine should be checked for secondary indication. If no secondaries are evident, engine may be used at the discretion of the aircraft commander for situations requiring power. Factors considered to continue engine operation should include, but are not limited to, weather, size and condition of runway (wet, winds, etc.), and other aircraft systems status. If secondaries are evident, perform the EMERGENCY SHUTDOWN CHECKLIST in paragraph 15.2. In both cases, land as soon as possible.

////////////////////////////////////////////

Profile:

KNGP

ASR 13R @ KNGP

PAR 13R @ KNGP

ILS 13R @ KNGP via D( RYNOL

ILS 13R @ KNGP via RV