INAV Review

- Name the following frequencies…

  - 225.0-399.95 MHz

    - UHF

  - 118.0-137.0 MHz

    - VHF Communications

  - 108.0-117.95 MHz

    - VHF Navigation Equipment

  - 108.1-111.95 MHz (Odd Tenths)

    - Localizer VHF

- What are the VOR receiver checkpoint limitations (Ground and Air)?

  - Ground - +/- 4 degrees

  - Air- +/- 6 degrees

- (T/F) Radios that are MHz are line of sight and not affected by weather.

  - True

- LF/NDBs have a frequency of ___ KHz, are not line of sight, and they are affected by weather.

  - 190-535 KHz

- What is the max distance of the DME?

  - 199 NM (slant range/ line-of-sight distance)

- How is station passage indicated on a VOR?

  - Flip of the to/from indicator

- How is station passage indicated on a TACAN?

  - Minimum DME

  - However, DME is a back-up if using a VORTAC (to/from is primary)

- With an identifier of “I-CRP,” what is the Morse code for identifying the LOM?

  - “CR”

- With an identifier of “I-CRP,” what is the Morse code for identifying the LMM?

  - “RP”

- What is the identifier and light color, for the OM?

  - “Dash, Dash, Dash“ and a blue light

- What is the identifier and light color, for the MM?

  - “Dash Dot, Dash Dot, Dash Dot” and Amber light

- What is the identifier and light color, for the IM?

  - “Dot, Dot, Dot” and White light

- What is the useable range for the localizer?

  - 18 NM

- What is the useable range for the glideslope?

  - 10 NM

- Is a VOR or a TACAN needed if flying in Class Bravo airspace?

  - Yes, but only if flying IFR

- Do we need a pilot’s license to fly in Class Charlie airspace?

  - NO

- What are the Class Alpha airspace dimensions?

  - 18,000 feet MSL – FL600

- What are the typical Class Delta airspace dimensions?

  - Surface-2500 feet MSL

- What is the max airspeed within 4 NM of Class Charlie and Delta airports?

  - 200 knots

- What are the two max airspeeds when talking about Class Bravo airspace?

  - 250 knots max inside

  - 200 knots max underneath

- In a non-radar environment, what is the initial call when about to give a position report?

  - Position, Altitude, ETE to next position

- Regardless of radar contact, what are the mandatory position reports?

  - (V)acating any previously assigned altitude for a new one

  - (A)pproach missed

  - (C)limb/descent less than 500 FPM

  - (A)ltitude change while operating on a clearance specifying “VFR on top”

  - (T)AS changing by 5% or 10 knots (whichever greater) from filed flight plan

  - H(O)lding

    - Time and altitude upon reaching a holding fix or a point to which cleared (Does not apply to military aviators in training environment)

    - When leaving any assigned holding fix or point

  - (R)andoms

    - Any loss in controlled airspace of VOR or TACAN receiver capability, complete or partial loss of ILS receiver capability, or impairment of air/ground communications capability

    - When encountering unforecasted weather, or hazardous conditions even if forecasted

  - (S)afety of flight is compromised

- If arriving early to a fix when lost comms and there is no EFC, what is the primary place to hold?

  - Hold in a depicted holding pattern

- What should you do if one is not available?

  - Hold on the approach radial, and make the pattern turns on the protected side of the approach

- Within ___ minutes of a holding pattern, begin to slow down.

  - Three minutes

- If you reach your clearance limit before your EFC, what should you do?

  - Hold until EFC is reached

- How many altimeters are required for IFR flight?

  - One

- On an IFR flight plan, if you are “cleared as filed,” can you deviate from your route and altitude?

  - You can deviate from the filled route, but maintain the last assigned altitude

- Where should you proceed if you experience lost comms during radar vectors?

  - Proceed to the area you were being vectored to

- VFR-ON-TOP is a ___ type of flight plan where the semi-circle rules apply.

  - IFR

- Can you deviate from your route or altitude during VFR-ON-TOP?

  - You may not deviate from the route

  - You may change altitude, but must report it first to ATC

- (T/F) After cancelling IFR, you still need to physically close your flight plan.

  - True

- Define HAT

  - The height above touchdown is the height of the DH or MDA, above the highest runway elevation in the touchdown zone

- Define HAA

  - The height above airport is the height of the MDA above published airport elevation

- What portion of the runway is included in the TDZE?

  - The first 3000 feet, regardless of runway length

- How many feet of protection do circling minimums guarantee?

  - 300 feet

- All the altitudes on an approach plate are MSL, except these three…

  - HAT

  - Weather ceiling

  - HAA

- What are the Navy takeoff minimums?

  - Precision: It is the published minimums for the approach, but cannot be lower than 200-1/2

  - Non-precision: It is the published minimums for the approach, but cannot be lower than 300-1

- Be able to explain the alternate minimums.

- According to OPNAV 3710.7, when can we descend below the MDA?

  - Runway environment insight

  - A safe landing can be executed

- If you are on an airway and cleared for an approach, when can you descend?

  - You can immediately descend to the MEA

  - You can descend to the approach plate altitude when established on a published segment of the approach

  - Remember to report all altitude changes to ATC

- Can we descend if not on an airway?

  - No, you must maintain the last assigned altitude until established on a published segment of the approach

- If going missed approach early, can we climb or turn?

  - You may initiate a climb, but you may not turn until the MAP

- If shooting a procedure turn approach, do we have to use the 45/180 method to reverse direction?

  - No.  You may do any type of maneuver that will reverse your course, and stay on the protected side of the approach

- What are the 5 mandatory “read backs” to ATC?

  - Heading an altitude if being vectored

  - Hold short

  - Position and hold

  - Altimeter if in the terminal area

  - Leaving an altitude

- If we are on a glideslope and encounter a strong headwind, what action should be taken in regards to the rate of descent?

  - Decrease your rate of descent so you do not descend below the glideslope

- How many marker beacons are in the TC-12?

  - Two

- Where is preferred routing located?

  - AP-1

- Where do VFR cruising altitudes begin?

  - 3000 feet AGL

- Will you receive priority handling if you declare minimum fuel?

  - No, you must declare an emergency

- For detailed information on approach information, where should you look?

  - TERPS

- Does IFR traffic have priority over VFR traffic?

  - No

- When accepting a visual approach, who is responsible for wake turbulence separation?

  - PIC

- What must be kept in mind when thinking about getting a contact approach (Special VFR)?

  - ATC will not initiate the call (the pilot must request it),

  - Need to remain clear of clouds; Must maintain 1 SM visibility

- Do you always need to use “straight-in” minimums when executing a “straight-in” approach?

  - No, a “straight-in” approach is any approach that does not use a PT

- What are the max holding speeds?

  - 0-6000 is 200 knots		6000-14,000 is 230 knots

Above 14,000 is 265 knots

- When can you sidestep to another runway when shooting an approach?

  - When runway environment is in-sight

- Aircraft must circle when ___ degrees of difference is between the FAC and runway.

  - 30 degrees

- What is the lowest a low altitude airway can be?

  - 1200 feet AGL

- What must be restated when receiving an abbreviated clearance from ATC?

  - They must restate destination, SIDs, and altitude

  - It is only good for the route