Metro Review

- What are the five weather observation techniques?

  - Sharp temperature changes over a relatively short distance

  - Change in moisture content

  - Rapid shifts in wind direction

  - Pressure changes

  - Clouds and precip patterns

- What is the source region and the corresponding temperature of the following…

  - A--------------------------------------Arctic/Coldest

  - P--------------------------------------Polar/Cold

  - T--------------------------------------Tropical/Warm

  - E--------------------------------------Equatorial/Warmest

- What do the following symbols mean?

  - M-------------------------------------Maritime/High moisture content

  - C--------------------------------------Continental/Low moisture content

- What is the air mass temperature, surface temperature and stability of the following symbols

  - W-------------------------------------Warm/Colder/Stable

  - K--------------------------------------Cold/Warmer/Unstable

- What weather would result from an air mass classified as mTw?

  - The resulting weather would produce considerable stratiform cloudiness, steady precipitation, fog, no turbulence, steady winds and rime icing

- What weather would result from an air mass classified as mTk?

  - The resulting weather would produce cumuliform clouds, good visibility, showers/thunderstorms, gusty winds, turbulence and clear icing

- What are the 3 general rules about fronts?

  - All fronts extend from low pressure centers

  - Winds will be parallel in advance and perpendicular behind a front

  - Pressure will fall before and rise after a frontal passage

- What types of clouds/weather are associated with a warm front?

  - Cirrus, cirrostratus, altostratus, nimbostratus and eventually, stratus, rain and fog

- What types of clouds/weather are associated with a cold front?

  - Cumulonimbus, altocumulus, and showery precipitation

  - Rapid clearing usually occurs with the passage of the front

- What is the weather associated with a stationary front?

  - Associated weather is most often that of a warm front

- Squall lines are defined as nonfrontal lone of thunderstorms or cumulonimbus clouds that develop __ - ___ miles ahead of a rapidly moving ____ front.

  - 50-300 miles

  - Cold front

- The squall line is characterized by what 6 weather phenomena?

  - Violent wind

  - Rain

  - Lightening

  - Thunder

  - Hail

  - Tornadoes

- Turbulence is characterized by violent up and downdrafts often obtaining speeds at ___ feet per second.

  - 200 fps

- Name the four types of turbulence.

  - Mechanical

  - Frontal

  - Thermal

  - Wind Shear

- Thunderstorm vertical currents may be strong enough to displace aircraft up and down vertically as much as ___ to ___ feet.

  - 2000 to 6000 feet

- Max turbulence usually occurs near the ___ of the storm between ___ and ___ feet and is most severe in ___.

  - Mid-level

  - 12,000 and 20,000 feet

  - Clouds of the greatest vertical development

- Severe turbulence is present not just within the cloud.  It can be expected up to ___ miles from severe thunderstorms and will be greater downwind than into the wind.

  - 20 NM

- Cumulus cloud icing can be expected at what temperatures?

  - -25 to 0 degrees Celsius

  - Shorter exposure time due to the updrafts

- When can you expect to see freezing rain?

  - Ahead of warm fronts in the winter

- Lightning strikes to aircraft commonly occur __ miles from an actual thunderstorm.

  - 50 miles

- Greatest when temperatures are __ to __ degrees.

  - -5 to 5 degrees Celsius

- Hail usually occurs during the ___ stage of cells having strong updrafts.

  - Mature stage

- Hail is normally encountered from ___ to ___ feet and has been encountered as high as ___ feet in clear air and as much as __ miles downwind.

  - 10,000-30,000 feet

  - 45,000 feet

  - 20 miles

- Structural icing to aircraft normally occurs when the ambient air temperature is generally in the range of ____ to ____ degrees, with relative humidity in excess of ___ %

  - 0 to -18 degrees Celsius

  - 80%

- Stratiform clouds consist of small droplets and from ___ ice.

  - Rime ice

- Cumuliform clouds contain large droplets creating ___ ice.

  - Clear or glaze ice

- Encounters with mixtures of cloud types, occluded fronts, will usually generate ___ ice.

  - Mixed ice

- What are the two main dangers of clear ice?

  - Weight and aerodynamic effect

- What weather is associated with a Microburst?

  - Heavy rain “wall of rain”

  - Virga- rain falling but not reaching the surface

  - Turbulence

  - Blowing dust

  - Rolling clouds

  - Wind shear alerts

  - PIREPS

  - Frequent lightening

- When are aircraft most vulnerable during a microburst?

  - During take-off, approaches, and go-arounds

- A microburst is an intense, highly localized downward flow with velocities of ___ to ___ feet per minute that may emanate below any convective cloud.

  - 2000-6000 fpm

- Microburst may last __ to __ minutes from the time the first downburst strikes the surface, until it reaches max intensity.

  - 5-10 minutes

- What are the 4 methods of thunderstorm avoidance?

  - Go Around (Most preferred)

  - Go over

  - Go under (1/3 of the distance between ground and base of clouds)

  - Go through (last resort- 4,000 to 6,000 FT AGL, lower 1/3 of the cloud, with indicated OAT of at least 5 degrees C)

- List the thunderstorm hazards:

  - Turbulence and hail (the 2 biggest hazards to aircraft)

  - Icing

  - Low ceiling and visibility

  - Microburst

- When are severe weather watches (WW) issued?

  - Funnel clouds or tornadoes

  - Severe thunderstorms, defined by frequent lightening and one or more of the following

    - 50 kts of wind or greater

    - ¾ inch diameter hail or larger

- What are the only 2 reasons that you can fly into a WW area?

  - A qualified forecaster reports that the WX is not developing as earlier forecast

  - The aircraft performance is such that it can safely climb over the problem WX system

- CNATRA Aviation Weather Warning (CAWW) will be issued in the absence of a WW or SIGMET, if the threat is within ___ miles of the training command

  - 100 miles

- When are CAWW’s issued?

  - Line(s) of thunderstorms (greater than 45% coverage)

  - Severe thunderstorms

  - Embedded thunderstorms

- What is a MWA?

  - Military Weather Advisory

  - Air Force version of a WW that uses color-codes to depict problem WX

- What colors on a MWA equate to a WW?

  - Red = tornadoes, waterspouts, or funnel clouds

  - Blue = severe thunderstorms (maximum wind gusts of 50 knots or greater and/or hail ¾ inch or greater in diameter) and locally damaging winds

- What are SIGMETS?

  - Significant meteorological information for all aircraft

- How long is a WST valid?

  - Similar to a WW except for the time period covered: usually 2 hours

  - Forecast for 4 hours

- When is a WST issued

  - Sent out 55 minutes after the hour

- What does a convective SIGMET (WST) cover?

  - Tornadoes

  - Line(s) of Thunderstorms

  - Hail ¾ inch diameter

  - Embedded thunderstorms

  - Thunderstorm areas greater than or equal to an intensity level of four , with an area coverage equal to or greater than 40% or more

  - Winds in excess of 50 kts

- How long is a WS valid?

  - Up to 4 hours

- What does a non-convective SIGMET (WS) cover?

  - Severe/Extreme nonconvective turbulence or clear air turbulence (CAT)

  - Severe icing not associated with thunderstorms

  - Widespread duststorms/sandstorms or volcanic ash lowering visibility to less than 3 SM

- When are AIRMETS issued

  - Moderate icing

  - Moderate turbulence

  - Ceilings of less than 1000 feet and/or visibility less than 3 SM affecting an area of over 50% at any time

  - Sustained winds of 30 knots or more at the surface

  - Extensive mountain obscurement

- What do the following AIRMETS mean…

  - Sierra-------------------------------IFR

  - Tango-------------------------------Turbulence

  - Zulu---------------------------------Freezing

- Area Forecasts (FA)are issued ___ times daily for ___ areas in the US.

  - 3 times daily for 6 specific areas

- All info in the FA is in feet ___  except areas identified as ___ and ___.

  - MSL

  - AGL and CIG

- PIREPS are a valuable source of information for weather conditions which are available by no other means.  All pilots are urged to cooperate and promptly volunteer reports on cloud bases, tops and layers; flight visibility; precipitation; visibility restrictions; winds at altitude; and temperature aloft.

- Is ceiling information available in a PIREP?

  - NO because PIREPS are only in MSL, so we can only get a cloud layer

- What is the OPNAV 3710.7 VFR Minimum?

  - 1000 and 3sm

- What is the alternate rule when filing IFR?

  - 1 hour before and 1 hour after, it needs to be above 3000 and 3sm

- What does the BECOM line in a TAF mean?

  - The first time is the valid time (used when determining an alternate)

  - The second line is the official line

- Forecasted period for a TAF in the US is…

  - 24 hours

  - International TAFs are slowly becoming 24 hour forecasts (however, they are issued variably)

- Winds in a TAF are true or magnetic?

  - True

- The surface analysis chart is a picture of ___ meteorological conditions.

  - Current

- What info can be found on a surface analysis chart?

  - Locations of fronts, highs, lows, troughs, squall lines, sky conditions, weather and visibility

- Low level significant weather prognostic charts will provide a __ and __ hour forcast of expected significant weather conditions expected at a stated time from ___ to ___ feet MSL.

  - 12 and 24 hour

  - Surface to 24,000 MSL

- Weather Depiction Charts are used to outline areas of __ and ___.

  - IFR and MVFR

- When a WW is shown on a Radar Summary Chart, how is it depicted?

  - Dashed box

- The winds aloft prognostic chart contains __ panels

  - Eight

  - It does no report 3000 feet (unlike the winds aloft forecast)

- What symbols are used on a winds aloft prognostic chart?

  - A wind shaft indicates wind direction

  - The # at the base is temperature in Celsius

  - The # of barbs at the end of the wind shaft indicate the wind velocity in knots

  - 99 indicates calm or light & variable

  - If the direction is over 36 (i.e. 705609), subtract 500 from the wind direction and add 100 to the wind velocity

- What is the primary cause of adverse weather?

  - Moisture

- What causes the major changes in weather?

  - Drop or rise in pressure

- What is an unscheduled in-flight advisory for severe weather within the next two hours?

  - CWA (Central Weather Advisory)

- This can be accessed by pilots with a current medical certificate toll-free in the US via computer.

  - DUATS

- TEL-TWEB provides prerecorded ___ and ___ information at selected locations.

  - Meteorological and aeronautical

- TEL-TWEB is made available primarily for preflight planning and the telephone number for this service can be found in the ___ and ___ telephone numbers section of the AFD.

  - Flight Service Station (FSS) and NWS

- Telephone Info Briefing System (TIBS) is provided by AFSS and provides continuous telephone recordings of ___ and ____ information.

  - Meteorological and aeronautical

- PATWAS is a continuous recording of ___ information.

  - Meteorological

- Normally the recoding contains a summary of data for an area within __ SM of the parent station.

  - 50 SM

- EFAS provides enroute aircraft with timely weather on ___ MHz.

  - 122.0 MHz

- TWEB provides the same information as TEL-TWEB and broadcasts continuously over selected low frequency nav aids at ___ to ___KHz.

  - 190-535 KHz

- What are three, in-flight, 2-way radio weather services?

  - EFAS

  - PMSV

  - DUATS

- Where can you obtain a WX brief?

  - Base WX station

  - Phone

  - Radio

- Where is information about PMSV located?

  - FIH – Section C

- What does VV indicate in a METAR?

  - Total obscuration – the # after VV is the vertical visibility in hundreds of feet AGL

- How are cloud tops measured?

  - In feet MSL

- Who is ultimately responsible for receiving a weather brief?

  - PIC

- The core of strongest winds in the jet stream is generally found between ___ and ___.

  - 25,000 and 40,000 feet

- Wind speeds in the jet stream sometimes reach ___ but are generally between ___ and ___.

  - 300 knots

  - 100-150 knots

- What are the dimensions of the jet stream?

  - 1000-3000 miles in length

  - 100-400 miles wide

  - 3000-7000 feet deep

- Jet stream CAT often occurs in patches about ___ feet deep, ___ miles wide, and ___ miles long.

  - 2000 feet deep

  - 20 miles wide

  - 50 miles long

- When talking about IR satellite pictures, high clouds are very cold so they appear ___, mid-level clouds are ___, and low clouds are ___.

  - White

  - Light shade of gray

  - Darker shade of gray

- The primary characteristic of low pressure areas as seen on satellite pictures is the ___ or ___ shaped cloud pattern.

  - Question mark or comma shaped cloud pattern

- What do satellite pictures indicate?

  - Areas of low/high pressure, mountain wave turbulence, jet streams, fog, and low clouds

- What do the colors indicate in an enhanced infrared satellite picture?

  - Different temperatures

- What does the airborne weather radar indicate?

  - Frozen and liquid forms of precipitation

- Describe the different airborne weather radar returns:

  - Scalloped edge-----------------------------------rapidly developing thunderstorms

  - Hook -----------------------------------------------funnel clouds and tornado type conditions

  - V-notch--------------------------------------------tornado and thunderstorms

  - Finger ----------------------------------------------hail shafts

- Prevailing visibility means you can see ___% of the horizon at any given time

  - 50%

- When looking at SLP, if the first number falls between 0-5, add ___ and if it falls between 6-9 add ___.

  - 10

  - 9

- With the “Open circle, with an X through it” symbol on many weather charts, how do we know if it is a total or partial obscuration?

  - Total obscuration will give us a ceiling, which would be located just under the symbol

- What does HIWAS broadcast?

  - Different in-flight weather advisories (WWs, AIRMETS, SIGMETS…)

- What are the Seven notable problems with CAT.

  - It cannot always be foreseen, so no warning

  - Usually it is mild in the cockpit, but more severe in the back

  - It can occur when there are no visible clouds

  - Aircraft radars cannot detect it

  - It is common at high altitudes, where cruising aircraft suddenly enter turbulent areas

  - Occurs in cloudless air between 23,000-39,000 feet

  - It is most severe over mountainous areas

The following questions refer to a DD 175-1

- What are the five parts of the DD 175-1?

  - Mission/Takeoff Data

  - Enroute Data

  - Terminal Forecast

  - Comments/Remarks

  - Briefing Record

- When looking at a DD-175, what two charts/documents would we look at to get Minimum Ceilings?

  - Weather Depiction Chart

  - Area Forecast

- For maximum tops refer to the ___ for observed data, and the ___ for forecast data.

  - Radar Summary Chart

  - Area Forecast

- These charts are used for forecasting thunderstorm activity.

  - Radar Summary Chart

  - Area Forecast

- The ___ provides teletype forecast for enroute precipitation, while the ___ gives an observed facsimile indication.

  - Area Forecast

  - Weather Depiction Chart

- What charts are good for turbulence?

  - Area Forecasts, In-flight Weather Advisories, LLSW Prog Charts, SIGMETS, AIRMETS

- What charts are good for the minimum freezing levels?

  - Area Forecast, Winds Aloft Forecast, LLSW Prog Chart, Winds Aloft Prognostic, Constant Pressure Charts

- Supporting information for icing could be obtained by checking the station model on the

  - Constant Pressure Charts

- The Terminal Forecast section of the DD 175-1 provides space for information about weather conditions at both your ___ and your ___ plus ___.

  - Destination

  - Alternate

  - Any planned intermediate stops

- The void time of the brief will be ___ after ETD time, not to exceed ___ from the time entered under “weather briefed,” or “rebriefed at”…

  - 30 minutes

  - 2 hours